| Corner Balance Specs: |  |
| --- | --- |
| Left Front: 1030 lbs Right Front: 1049 lbs |
| Left Rear: 791 lbs Right Rear: 708 lbs |
| Cross Weight: 51.4% |  |
| Left Weight: 50.9% |  |
| Total Weight: 3577 lbs (Including 150 lb driver) |
| Ride Height |  |
| Left Front: 25 1/2 inches Right Front: 25 1/2 inches |
| Left Rear: 25 5/8 inches Right Rear: 25 5/8 inches |
| Alignment Specs: |  |
| Camber |  |  |
| Left Front: -3 Right Front: -3 |
| Left Rear: -2.6 Right Rear: -2.6 |
| Toe |  |  |
| Front: 1/16 out | Rear: 1/16 in |
| Caster |  |  |
| -5 |  |  |
| Sway Bar Settings |  |
| Front: Full Soft Rear: Full Stiff |